## Slide 1: Scalable-I/O Virtualization (SIOV) R2 Overview OCP Workstream Server Project October 2022 Contact Point: siovr2.admin@opencompute.org

## Slide 2: What is Scalable I/O Virtualization (SIOV)?
SIOV is hardware-assisted I/O virtualization designed for the hyperscale era, with the potential to support thousands of virtualized workloads per server.
  SIOV moves the non-performance-critical virtualization and management logic off the device and into the virtualization stack. It uses a new scalable identifier on the device to address the workloads’ memory.
SIOV delivers key benefits vs. prior art:
  Reduces the per-VM virtualization cost on the devices
  More efficiently supports large numbers of VMs and containers
  Provides more flexibility to the virtualization stack for provisioning & composability.
Impact: Virtualized I/O devices become much more configurable and scalable while delivering near-native performance to each VM/container/microservice.

## Slide 3: Why Scalable I/O Virtualization (SIOV)?
SIOV enables virtualization modernization of I/O devices (PCIe, CXL, etc.) for today’s massive-scale clouds
  SIOV is much more scalable and flexible than previous technologies, providing efficient I/O access to potentially thousands of containers or virtual machines
  SIOV is simpler and more efficient to implement and deploy for I/O device manufacturers, software providers and cloud operators
Driving as a standard enables an open ecosystem that fuels adoption, growth, and innovation
  Host Devices
  Target Devices
  Software & Operating Systems

## Slide 4: SIOV R1 Contribution & R2 Workstream Plan
Intel & Microsoft contributed SIOV R1 to OCP to encourage an open ecosystem hyperscale I/O virtualization
  Scalable I/O Virtualization
  https://www.opencompute.org/documents/ocp-scalable-io-virtualization-technical-specification-revision-1-v1-2-pdf
Arm, AMD, Broadcom, Intel, Microsoft & Red Hat formed an OCP SIOV R2 workstream to drive a broader ecosystem & further enhance data center I/O virtualization
  High level Scope:
    Ensure definition is compatible across multiple host and device architectures to provide a consistent usability experience.
    Ensure definition meets new, emerging, and complementary usages.
    Ensure a viable ecosystem transition path to SIOV Revision 2.0.

## Slide 5: SIOV R2 Workgroup Scope
Ensure Specification is compatible across multiple host and device architectures to provide a consistent usability experience. Key focus areas:
  Standard method for Assignable Device Interface (ADI) identification and enumeration, and ADI resource management (e.g. address spaces and interrupts)
  Standard methods for scaling ADI usage to future virtualization deployments (e.g. efficient/scalable interrupts or notifications, performance scaling, host/device communication efficiencies)
  Reference software implementations of the Specification
  If necessary, propose revisions to the generic mechanisms provided by other standards to ensure ecosystem interoperability with SIOV Revision 2.0 virtualization model
  Quality of Service (QoS) associations and management for ADIs
  Reliability, Availability, and Serviceability (RAS) capabilities and expectations
  Privilege/execution levels of virtualization software to enable optimal device resource management and isolation properties
Ensure Specification meets new, emerging, and complementary usages. Key focus areas:
  Extensions to support confidential computing (trusted execution) with ADIs
  Extensions to optimize live migration of virtual devices backed by ADIs
  Enhancements to Address Translation Services (ATS) for ADIs
  Extending support and interoperability to Peer-2-Peer (P2P) topologies
Ensure a viable ecosystem transition path to SIOV Revision 2.0. Key focus areas:
  Backward compatibility to SIOV Revision 1.0
  Heterogeneous deployment and coexistence of devices within a system, including SR-IOV, SIOV Revision 1.0, and SIOV Revision 2.0 target devices
  Ensure that key properties of prior virtualization models have reasonable corollary properties in SIOV Revision 2
  Specific transition guidance (e.g. SR-IOV to SIOV Revision 2.0 device transition guidance)

## Slide 6: SIOV R2 Workgroup Participation
Workgroup members have aligned to:
  Scope focus (prior slide and incorporate into CLA)
  Operating governance model
  Public distribution of specification at version 0.7 (and beyond)
  Expanding to new membership after releasing 2 public versions (0.7, 0.8)
    New membership requirements:
      Written details of intended contribution (actual IP, participation, deliverables) from new member
      75% majority existing member approval required to accept
      Signature of existing CLA, unmodified (includes/aligns to scope)

## Slide 7: BACKUP

## Slide 8: SR-IOV (Single-Root I/O V) 🡪 Scalable I/O Virtualization (Scalable-IOV)
Arbiters
…
IOMMU
VM 1
VM 2
VM 3
VM n
…
Hardware Replicated Virtual Functions
VF 1
VF 2
VF 3
Traditional SR-IOV Device
Compute Engines
I/O Engines
VF n
Hypervisor
Arbiters
…
IOMMU
Scalable-IOV Capable Device
Compute Engines
I/O Engines
…
…
Assignable Device
Interfaces (ADIs)
Hypervisor / Orchestration
…
VM 1
Container 1
VM x
Container x
VM x
Container x
VM p
Container p
While SR-IOV maps virtual devices as Virtual Functions (VFs) in HW, S-IOV composes virtual devices through light-weight and scalable Assignable Device Interfaces (ADIs) for fast-path operations and software mediated slow-path operations
I/O Interface Agnostic (PCIe, CXL, etc.)
PCIe

## Slide 9: Scalable IOV Benefits
Process
Q
Q
Q
Q
Q
Q
Q
Q
Device
VDEV1
VDEV2
VM
Container
Process
syscall
Flexibility
Over-provisioning
Q
Q
Q
Q
Q
Q
Q
Q
Device
VDEV1
VDEV2
Scalability
Q
Q
Q
Q
Q
Q
Q
Q
Device
VDEV1
VDEV2
VM1
VM2
VDEVn
…
VMn
…
Composability
Q
Q
Q
Q
Device
Q
Q
Q
Device
VDEV
VM
VDEV
VM
Live Migration
Notes: Page #

## Slide 10: Scalable IOV: High Level Software Architecture
Device specific VDCM to decide what to intercept vs direct map
Emulating infrequent operations in VDCM simplifies device without compromising performance
Host Driver
Guest Driver
Virtual Device Composition Module
(VDCM)
IOMMU
(w/ Scalable IOV
extensions)
VMM
Hosting
Device
Function
ADI
ADI
ADI
ADI
………………….....
PASID
PASID
Frequent
Direct Mapped Operations
Host
Guest
VDEV
ADI
ADI
Infrequent
Host Intercepted Operations
Device-specific software components
Q
………
Backend Resources
Q
Q
Q
AI Resource Mapping
VM Manager