## Slide 1: OCP Open Accelerator Infrastructure Overview

## Slide 2
OAI Overview
OAI Group Workstreams
OAI OAM/UBB Spec
OAI Monthly Call
Agenda

## Slide 3: OAI Overview
Formed 3/2019, under OCP Server Project
To build the infrastructure for fast adapting, upcoming products for AI and HPC application

## Slide 4: OAI Group Workstreams
OAI System
    UBB/OAM spec maintain and update, HIB/Chassis spec ,System firmware requirements
Power
    Focus on Power delivery of OAI, including power requirement, design specs, recommended practice, reference designs, etc.
Cooling
    Establish specifications, framework, standardization and best practices of Liquid Cooling Solutions for OAI and OAM, from module level to system level; Interchangeable OAM liquid cooling cold plates and OAM cards, and fully integrated liquid cooling modules in a server chassis
High Speed
    OAM2.0 spec, Next Gen high speed research such as 112G PAM4, PCIe Gen5/6, OAI system design high speed related
OAMTool
    Common vendor-agnostic utility for OAM management

## Slide 5: OAI Workstreams Members
Facebook
Baidu
Microsoft
Intel
AMD
Inspur
Supermicro
Enflame
Luxshare
TE
Molex
Amphenol
Nallasway
Wiwynn
ZT Systems
Cooler Master
Microchip
Renesas
Microchip
STMicro
Artesyn
Xilinx
Intel Habana

## Slide 6
102mm x 165mm Module Size
12V and 54V/48V input DC Power
Up to 350w (12V) and up to 700w (54V/48V) TDP
    Air-cooled - Up to 450W
    Liquid-cooled – 700W
Up to eight x16 Links (Host + inter-module Links)
System management and Security Requirements
OAM Spec v1.1

## Slide 7
OAM ISO View

## Slide 8
OAM
Nvidia
OAM
AMD
OAM
Xilinx
Gaudi OAM
Intel/Habana
OAM
Enflame
OAM
Cambricon
OCP Accelerator Module

## Slide 9
8* OAMs in UBB
19’’ and 21’’ rack compatible
Interconnect topologies
Host Interface with retimers
Scale-out with Phy retimers
12V or 54V/48V power delivery
Debug/management interface
585mm(23.03”)
417mm(16.42”)
OAM1
OAM2
OAM5
OAM6
OAM 0
OAM3
OAM4
OAM7
Retimer
QSFP-DD
QSFP-DD
QSFP-DD
QSFP-DD
QSFP-DD
QSFP-DD
QSFP-DD
QSFP-DD-
ExaMAX 6p8c
2x2 power conn 54V/48V
2x2 power conn
54V/48V
power conn 12V
power conn 12V
Guide pin
PHY Retimer
PHY Retimer
UBB Spec v1.0

## Slide 10
UBB can support various topologies
Interconnect Topology
P0
P3
P4
P7
P1
P2
P5
P6

## Slide 11
OAI Reference Systems

## Slide 12
Join Us
Project Wiki : https://www.opencompute.org/wiki/Server/OAI
How to get involved : https://ocp-all.groups.io/g/OCP-OAI
OAI Project Monthly Call : 2nd Wednesday of every month 8-9am PST