Silicom - OE310G2I71-XR

Dual Port SFP+ 10 Gigabit Ethernet OCP Mezzanine Card Specification

August 2016

Author: Yossi Mimran

Rev 0.1

Scope

This document defines the technical specifications for Silicom Dual SFP+ 10 Gigabit Ethernet Open Compute Project (OCP) mezzanine card used in Open Compute Project.

Contents

License	3

1.	Key Features	4

1.1	Host Interface:	4

1.2	Form Factor:	4

1.3	Mezzanine Card Connector:	4

1.4	Performance Features:	4

1.5	LAN and Virtualization Features:	4

2.	Functional Description	5

2.1	Block diagram	5

2.2	Block Diagram Overview	5

2.3	Chips-Set:	6

2.4	Power	6

2.5	Management Connection	7

2.6	NC-SI over RMII Connection	7

2.7	Mezz FRU EEPROM	8

2.8	Thermal Reporting Interface	8

3.	Mezzanine Card Form Factor	9

3.1	Mechanical Description	9

3.2	Mezzanine Card Connectors	10

3.3	Port and LED location	10

4.	Environmental	11

4.1	Environment Requirements	11

4.2	Regulatory Compliance	11

5.	Compliance to OCP_Mezz 2.0_rev1.00 specification	12

6.	Revision History	12

Overview

This document defines the technical specifications for the Silicom Dual Port SFP+ 10 Gigabit Ethernet Open Compute Project (OCP) mezzanine card used in Open Compute Project.

Silicom’s Dual Port SFP+ 10 Gigabit Ethernet Open Compute Project (OCP) mezzanine card designed for use in any mother board that can utilize “OCP_Mezz 2.0_rev1.00” MEZZ cards.

Silicom Dual Port SFP+ 10 Gigabit Ethernet OCP mezzanine card is based on Intel XL710 Ethernet controller with fully integrated Gigabit Ethernet Media Access Control (MAC) and SFI Interface. In addition to managing MAC and PHY Ethernet layer functions, the controller manages PCI Express packet traffic across its transaction, link, and physical/logical layers. Using hardware acceleration, the controller offloads tasks from the host, such as TCP/UDP/IP checksum calculations and TCP segmentation.

Silicom Dual Port SFP+ 10 Gigabit Ethernet OCP mezzanine card implement a type C NC-SI interface (single package, common bus buffers and shared RX queue).

# License

As of June 16 2016, the following persons or entities have made this Specification available under Open Compute Project Hardware License (Copyleft) Version 1.0 (OCPHL-R), which is available at http://www.opencompute.org/community/get-involved/spec-submission-process/

Silicom Ltd.

You can review the signed copies of the Contributor License for this Specification at on the OCP website which may also include additional parties to those listed above.

Your use of this Specification may be subject to other third party rights. THIS SPECIFICATION IS PROVIDED "AS IS." The contributors expressly disclaim any warranties (express, implied, or otherwise), including implied warranties of merchantability, non-infringement, fitness for a particular purpose, or title, related to the Specification. The entire risk as to implementing or otherwise using the Specification is assumed by the Specification implementer and user. IN NO EVENT WILL ANY PARTY BE LIABLE TO ANY OTHER PARTY FOR LOST PROFITS OR ANY FORM OF INDIRECT, SPECIAL, INCIDENTAL, OR CONSEQUENTIAL DAMAGES OF ANY CHARACTER FROM ANY CAUSES OF ACTION OF ANY KIND WITH RESPECT TO THIS SPECIFICATION OR ITS GOVERNING AGREEMENT, WHETHER BASED ON BREACH OF CONTRACT, TORT (INCLUDING NEGLIGENCE), OR OTHERWISE, AND WHETHER OR NOT THE OTHER PARTY HAS BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGE.

# Key Features

## Host Interface:

- Supports OCP Mezzanine card 2.0 Design Specification 1.00

- Supports PCI-Express Base Specification Revision 3.0 (8GT/s)

- PCI Express Gen 3.0 X8 lanes in Connector A

## Form Factor:

Open Compute Project Mezzanine Card, Type 1

## Mezzanine Card Connector:

Bergstak Plug 4 FCI 61083-124402LF or equivalent.

## Performance Features:

- Support for jumbo frame up to 9.5KB

- Flow control support

- Priority Flow Control (draft IEEE 802.1Qbb)

- Enhanced Transmission Selection (draft IEEE802.1az)

- Statistics management and RMON

- 802.1q VLAN support

- DCB/DCB-X support

- Message Signal interrupts (MSI-X)

- Storage - Enabling competitive performance with native OS intelligent offload solutions, including NAS, iSCSI and FCoE

## LAN and Virtualization Features:

- Network Virtualization offloads for VXLAN and NVGRE

- Unified Networking Providing a single wire for LAN and storage: NAS (SMB, NFS) and SAN (iSCSI, FCoE)

- Virtual Bridging Support – VEPA/802.1Qbg, BPE/802.1Qbh

- Physical Functions – Up to 8 per port, up to 16 per device

- Support for 128 Virtual Device Queues (VMDq) per port

- Hardware Queue Pairs – Up to 1.5K (non-RDMA); up to 256K (RDMA)

- Virtualization - Alleviating hypervisor I/O bottlenecks by providing flow separation for Virtual Machines (VMs)

- TCP/IP/L2 features:

- Receive Side Scaling (RSS)

- Large Send Offload (LSO)

- TCP/UDP/IP/SCTP Checksum Offload

- IPV4, IPV6

# Functional Description

## Block diagram

- Block Diagram

## Block Diagram Overview

The Dual Port SFP+ OCP Mezzanine Card is based on Intel XL710 (Dual port 10G Ethernet MAC and SFI PHY). The MAC+ PHY interfaces the PC / Server via its PCI-Express interface with a X8 Lane.

The PCI- Express adapter employs 2 ports. Each port transports 10Gb/s transmit and 10Gbit/s receive, which gives 20 Gbit/s double simplex transportation.

The Ethernet port has indication LED: for Activity / Link Speed.

On board power supply circuitry generates the 5V, 3.3V, 0.935V, 0.85V.

## Chips-Set:

Intel FTX710-BM2: Dual 10 Gigabit Ethernet Controller – 576 ball FCBGA 25mmx25mm

Optical Media options:

(2) Finisar SFP+ FTLX8574D3BCV (or compatible), 1/10Gigabit Multi Mode optical transceiver Pluggable transceiver with press-fit and heat-sink cover

(2) Finisar SFP+ FTLX1471D3BCV (or compatible), 1/10Gigabit Single Mode optical transceiver Pluggable transceiver with press-fit and heat-sink cover

BGA Chips Set count: 1

## Power

Without Transceivers

| Current Rating | S5 | TDC - S0 | IPeak- S0 |
| --- | --- | --- | --- |
| P12V_AUX/P12V | TBD | TBD |  |
| P5V_AUX | N/A | N/A |  |
| P3V3_AUX | TBD | TBD |  |
| P3V3 | N/A | N/A |  |
| Total Card Power | TBD | TBD | 5.63W |

With SR transceivers

| Current Rating | S5 | TDC- S0 | IPeak - S0 |
| --- | --- | --- | --- |
| P12V_AUX/P12V | TBD | TBD |  |
| P5V_AUX | N/A | N/A |  |
| P3V3_AUX | TBD | N/A |  |
| P3V3 | N/A | N/A |  |
| Total Card Power | TBD | TBD | 7.30W |

With LR transceivers

| Current Rating | S5 | TDC - S0 | IPeak - S0 |
| --- | --- | --- | --- |
| P12V_AUX/P12V | TBD | TBD |  |
| P5V_AUX | N/A | N/A |  |
| P3V3_AUX | TBD | TBD |  |
| P3V3 | N/A | N/A |  |
| Total Card Power | TBD | TBD | 7.602W |

## Management Connection

The board shall support both RMII based NC-SI and SMBus for OOB.

Intel XL710 can support:

- connection via legacy SMBus

- Connection via NC-SI over RMII

- Connection via NC-SI over MCTP. This connection can be over SMBus, PCIe or both.

- Two connections — A connection via NC-SI over RMII for pass-through traffic and a connection via MCTP used only for control traffic

By default, the XL710 will be configured to support two connection: NC-SI over RMII for pass- and a connection via MCTP over SMBUS.

- Management Connection

## NC-SI over RMII Connection

| NC-SI Signal | Intel X710 | Mezzanine Connector |
| --- | --- | --- |
| NCSI_RCSDV | AB11 (NCSI_CRS_DV) | A14 |
| NCSI_50M_RCLK | AC11 (NCSI_CLK_IN) | A15 |
| NCSI_TXEN | AB10 (NCSI_TX_EN) | A16 |
| NCSI_RXD0 | AA11 (NCSI_RXD_0) | A22 |
| NCSI_RXD1 | AC10 (NCSI_RXD_1) | A23 |
| NCSI_RXER | (No compatible signal) | A78 |
| NCSI_TXD0 | AA10 (NCSI_TXD_0) | A80 |
| NCSI_TXD1 | AD11 (NCSI_TXD_1) | A81 |

## Mezz FRU EEPROM

The adapter shall support FRU EEPROM on Mezzanine card

- Mezz FRU interface: A18, A19

- FRU EEPROM: ATMEL AT24C01C (1Kbits)

- Slave Address: 0xA2

- Mezz ID Byte : 0x00 (8 lanes of PCIe on Connector A)

- Mezz Capability Byte : 0x00 (Single Host PCIe Mezz)

- The connection diagram is shown in figure 3.

- Mezz FRU EEPROM

## Thermal Reporting Interface

The adapter shall support On die temperature sensing interface

- Thermal report Interface: A75, A76

- Thermal report Type: On die Temperature sensing

- Thermal sensing device: TMP421

- Slave Address: 0x3E

- The connection diagram is shown in figure 4.

- Remote on die temperature sensing

# Mezzanine Card Form Factor

## Mechanical Description

- The Mechanical outline conforms with base Design: P1 - Single/Dual ports 10G/25G SFP+/SFP28

- Stack Type Support: Type 1

- Controller IC on primary side.

- PCB Mechanical Drawing is shown in figure 5

- The Product includes Passive heatsink

- PCB Mechanical Drawing

.

## Mezzanine Card Connectors

- Connector A: Used

- Connector B: Not Used

- Connector B PCB Area: Not Available

- Connector C: Not Installed

- Network I/O: Two single SFP+ Cages

- Mezzanine card Connector: Bergstak Plug 4 - FCI 61083-124402LF or equivalent.

## Port and LED location

- LEDs placement within "P1 - Single/Dual ports 10G/25G SFP+/SFP28" envelope.

- Ports and LEDs Location and Numbering:

- Ports and LEDs location and numbering

- LEDs definition:

Each Port has 2 LEDs to indicate link status and speed.

Link:  	Physical link Speed:

Green stay on – physical link on with 10G Speed

Yellow stay on - physical link on with 1G Speed

Off – physical link off.

Link /ACT: Logic Link/Activity, Green

Green stay on – logic link up, no activity

Green blinking – logic link up, activity

Off – logic link off

# Environmental

## Environment Requirements

- Operating and Storage Humidity: 0%–90%, non-condensing

- Ambient Operating Temperature: 0°C – 55°C (32°F – 131(F)

- Air Flow: minimum of 100 LFM

- Storage Temperature: -20(C–65(C (-4(F–149(F)

## Regulatory Compliance

- FCC 47CFR Part  15:2013, Subpart B Class B

Conducted emissions

Radiated emissions

- EN 55022: 2010, Class B

Conducted disturbance at mains terminals

Conducted disturbance at telecommunication port

Radiated disturbance

- EN 61000-3-2: 2006+A1(09)+A2(09)

Harmonic current emissions

- EN 61000-3-3: 2008

Voltage fluctuations and flicker

- EN 55024: 2010

Immunity to electrostatic discharge (ESD)

Radiated immunity to radio frequency electromagnetic field

Conducted immunity to electrical fast transients / bursts (EFT/ B)

Conducted immunity to voltage surges

Conducted immunity to disturbances induced by radio frequency field

Conducted immunity to voltage dips and short interruptions

# Compliance to OCP_Mezz 2.0_rev1.00 specification

- Deviation from the specifications: none.

- Power Capability: Legacy Implementation of Mezzanine Card (P12V_AUX)

# Revision History

| Author | Description | Revision | Date |
| --- | --- | --- | --- |
| Yossi Mimran | Initial Draft Spec | 0.1 | 21-Aug-2016 |