## Slide 2
Redfish and OCP Topics
Jeff Autor
Co-Chair, DMTF SPMF
Distinguished Technologist, Hewlett Packard Enterprise

## Slide 3
Disclaimer
The information in this presentation represents a snapshot of work in progress within the DMTF.
This information is subject to change without notice. The standard specifications remain the normative reference for all information.
For additional information, see the Distributed Management Task Force (DMTF) website.

## Slide 4: Scalable Platforms Management Forum
Created in September 2014 – now 22 member companies
Co-Chairs: Jeff Autor (HPE), Paul Vancil (Dell)
Promoters: Broadcom Limited, Dell, EMC, Emerson, Hewlett Packard Enterprise, Intel, Lenovo, Microsoft, Supermicro, VMWare
Supporters: AMI, Fujitsu, HGST, Huawei, IBM, Insyde Software, Mellanox, NetApp, Oracle, Microsemi, Qualcomm, Seagate
Charter: Create and publish an open industry-standard specification and schema that meets the expectations of Cloud and Web-based IT professionals for scalable platform hardware management utilizing existing tool chains as well as being usable by personnel with minimal experience.
Alliance Partnerships
                OpenCompute Project
                UEFI - Collaborating on Firmware Update and Host Interface work
                SNIA – Collaborating on Storage modeling / alignment between SSM and Redfish

## Slide 5: Redfish Specification
RESTful interface over HTTPS in JSON format based on OData v4
Usable by client applications and browser-based GUIs
A secure, multi-node capable replacement for previous interfaces
Schema-backed human-readable output
Covers popular use cases and customer requirements
Intended to meet OCP Remote Machine Management requirements

## Slide 6: Redfish v1.0 Specification & Schema
Retrieve “IPMI class” data
Basic server identification and asset info
Health state
Temperature sensors and fans
Power supply, power consumption and thresholds
  Discovery
  Service endpoint (network-based discovery)
  System topology (rack/chassis/server/node)
  Basic I/O infrastructure data
  Host NIC MAC address(es) for LOM devices
  Simple hard drive status / fault reporting
  Security
  Session-based, leverages HTTPS
  Perform Common Actions
Reboot / power cycle server
Change boot order / device
Set power thresholds
  Access and Notification
Serial console access via SSH
Event notification method(s)
Logging method(s)
BMC infrastructure
View / configure BMC network settings
Manage local BMC user accounts

## Slide 7: Redfish releases
v1.00 Released August 2015
  Specification and Schema files
v1.01 Errata Release November 2015
  Clarifications to specification, corrected errors in schemas
v1.10 Schema release November 2015
  Additions to ComputerSystem, Chassis
v1.02 Errata – in Progress
  Will correct schema naming issues (all schemas will be revised)
  Clarifications to specification
  Expected in Spring 2016 (March/April)
Releases planned for Schema and Specification
  Summer 2016 (July/August)
  Fall 2016 (November)

## Slide 8: SPMF Work in Progress
Significant expansion to data model coverage
  PCIe devices
  Storage subsystems
  Network Adapters / Controllers
  DIMM / NV-DIMM inventory
“Task Force” sub-groups created to tackle specific topics
  Host (OS) Interface to Redfish – working with DMTF PMCI
  Firmware Update – working with UEFI and DMTF PMCI
  Storage – working with SNIA
  Privilege Mapping
“Integration recipe” target for Redfish implementations
  Strong desire for an OCP HW Management conforming property list
  Other groups welcome to suggest target recipes

## Slide 9: Redfish Ecosystem – Tool Development underway
Github public repository
Coming soon!
Client Library
Common utility support functions
  Discovery, Enumeration, etc.
  Event subscription
Typical tasks
  Power on/off/reboot
  Gather thermal data
Languages under consideration
  Python
  Java
  PowerShell
  Other possibilities…
Command Line Utility
Similar to IPMItool
Designed for end users
Calls Client library
Conformance Test Suite
Schema-aware tool for testing
Checklist for vendors and customers
Avoid spec interpretation conflicts
Schema Dev Tools
CSDL Validator
CSDL to JSON-Schema converter

## Slide 10: “Catfish” Mockup for OCP
Mockup of a monolithic server with a Redfish implementation aligned with OCP Remote Machine Management Spec 1.01
  One ComputerSystem
  One Chassis
  One Manager
Provides basic management features :
  Power-on/off/reset
  Boot to Pxe, HDD, BIOSsetup (boot override)
  4 temp sensors per DCMI (CPU1, CPU2, Board, Inlet)
  Simple Power Reading, and DCMI Power Limiting
  Fan Monitoring w/ redundancy
  Set asset tag and Indicator LED
  Basic inventory (serial#, model, SKU, Vendor, BIOSver…)
  User Management
  BMC management: get/set IP, version, enable/disable protocols

## Slide 11: “Catfish” mockup discussion
What Catfish does not have that Redfish 1.0 model supports:
  No PSUs in model (RMM spec did not include PSUs)
  No ProcessorInfo, MemoryInfo, StorageInfo, System-EthernetInterfaceInfo
  No Tasks
  JsonSchema and Registries collections left out (since that is optional)
  No EventService
    Remote Machine Management spec used basic PET alerts
Discussion
  Opportunity to define some Redfish ‘Integration Recipes’ that specify
  What APIs and properties are supported / required
  How to capture

## Slide 12: Redfish Resource Explorer
Browser-based Educational tool part of the DMTF web site for Redfish
Explore “mockups” of the Redfish data model
Navigate via links through the model to various resources
Text descriptions are taken directly from the schema files for consistency
http://redfish.dmtf.org

## Slide 13: More information and Providing Feedback
Download Specification and Schema: http://www.dmtf.org/redfish
Redfish Developer Information Site: http://redfish.dmtf.org
BrightTalk webinars: https://www.dmtf.org/education/webinars
  Introduction to Redfish (25min)
  Redfish Data Model Deep Dive (55min)
  Modeling the Redfish Way (60min)
Provide feedback through the DMTF feedback portal, on both published specification and “Work in Progress”: http://www.dmtf.org/standards/feedback
Coming Soon – public User Group / Forum
Join the SPMF
  By Joining the DMTF and SPMF, you can shape the standard
  http://www.dmtf.org/join/spmf

## Slide 15: Introduction to the Redfish data model
All resources linked from a Service Entry point (root)
  Always located at URL: /redfish/v1/
Major resource types structured in ‘collections’ to allow for standalone, multi-node, or aggregated rack-level systems
  Additional related resources fan out from members within these collections
ComputerSystem: properties expected from an OS console
  Items needed to run the “computer”
  Roughly a logical view of a computer system as seen from the OS
Chassis: properties needed to locate the unit with your hands
  Items needed to identify, install or service the “computer”
  Roughly a physical view of a computer system as seen by a human
Managers: properties needed to perform administrative functions
  aka: the systems management subsystem (BMC)

## Slide 16: Resource map (highlights)
Root Resource
/redfish/v1/
Links to all content
Collection of Chassis
/redfish/v1/Chassis
“Physical” view of the system
Chassis
/redfish/v1/Chassis/<id>
Chassis global physical asset info
Collection of Managers
/redfish/v1/Managers
BMC functionality
BMC
/redfish/v1/Managers/<id>
System Manager operations
1..n
Collection of Systems
/redfish/v1/Systems
“Logical” view of the system
Server Information
/redfish/v1/Systems/<id>
Model #, Serial #, Boot Order, NIC MAC, status, etc.
1..n
1..n
Processors
Disks
NICs
Power
Thermal
Services
Logs
Session Service
Account Service
JSON Schemas
Event Service