## Slide 1: OCP Switch HW-Specific Chipset Software Architecture Challenge
September 16, 2015
DRAFT

## Slide 2: Problem Statement
Innovative use of OCP-based bare metal or white box switches is currently a challenge/opportunity due to lack of optimal SW architecture.
There are dependencies of the chipset SW on the specific switch HW and thus even small patches or minor features must go though a cycle of development and testing at the chipset SW supplier (e.g., OF-DPA at Broadcom) and the HW provider’s ‘HW specific chipset SW’ (e.g., Accton).
If the switch user finds an issue the cycle repeats: “User – ODM/Supplier – Chipset Supplier”. This results in delays and difficulty in solving issues or innovating.
Switch Merchant Silicon
Chipset
Chipset SW w/HW specifics
OF Agent
Chipset SW API
OpenFlow
OCP
Software
-
ONL
ONIE
OCP Bare Metal Hardware
Chipset SDK API
Generic Example
How can industry collaborate to improve innovation and speed?
HW specific Chipset SW development and test
Chipset SW development and test
Switch User testing issue or innovation

## Slide 3: Potential Solutions for Discussion
Short Term:
Ask chipset suppliers to include OCP-based HW/SW (including ONL/ONIE) reference switches in their Chipset SW testing
Mid/Long Term:
Improve industry’s ability to dynamically improve the HW specific Chipset SW as driven by innovation and testing through improved SW architecture
Look at how similar issues were solved in the past:
    E.g., Standardize modularization/layering following example of server BIOS used to express HW specifics (if switch HW suppliers had a standard way to express their HW specifics it could avoid switch HW maker editing every chipset SW patch, etc into a HW specific version of the chipset SW)

## Slide 4: Next Steps
If community agrees this is an opportunity to improve OCP Switch innovation velocity, possible next steps include:
Form a Ad-hoc or BoF that includes representatives of users, chipsets, and switch makers to refine the problem statement and potential short and longer term improvements
    Document and propose to OCP highest potential improvements
    Try out and refine then propose formal SW architecture and requirements improvements
    Etc.