## Slide 1
SPIRAL Protocol Family
Xiaoyu Ruan and Will Stevens
{xiaoyu.ruan; william.a.stevens}@intel.com
For OCP security forum
Jan. 29, 2019

## Slide 2: USB Type-C Authentication Protocol and Its Application in Cerberus
Image credit: Project Cerberus Challenge Protocol

## Slide 3: A Good and straightforward Protocol. But Anything to Improve?
Authentication and key agreement require (expensive) asymmetric key operation every boot – RSA or ECC. Not prefect for performance sensitive applications, e.g., secure boot.
Easy problem! Just save the shared secret in secure NVM on both sides for future use.
What if responder does not have secure NVM? e.g., CPU
Our Goal: Design a protocol that
Does not require asymmetric operation after initial pairing between initiator and responder
Does not require secure NVM on responder

## Slide 4: The Main Idea
Primary idea: responder wraps shared secret (SK) with its own secret key (SSTn) and sends to initiator to store.
Prerequisite: responder FW has a secret key from ROM. The secure key changes per FW security version SVN.
Responder flow during boot
* The fuse / PUF used for private credential derivation is leveraged for SSTn derivation.

## Slide 5: SPIRAL-OneWay : Initiator Authenticates Responder
See Backup for flow when responder does not have DRNG

## Slide 6: SPIRAL-TwoWay: Mutual Authentication
Responder is required to have DRNG in order to authenticate initiator.

## Slide 7: Cerberus: Backward Compatibility / Discovery
Use one reserved bit in Device Capabilities Request and Response to indicate if SPIRAL is supported

## Slide 8: Next Steps
Review at OCP, DMTF, and PCIe forums and discuss adoptions in their specifications.
Forum | Date | Status
DMTF | 1/22/2019 | Done. Reviewers from Intel, Lenovo, Cisco, HPE, Mellanox, Dell, Microchip, ARM, Marvell, Broadcom
OCP | 1/29/2019 | 
PCIe | ?? | 

## Slide 9: Backup

## Slide 10: SPIRAL-OneWay : When Responder Doesn’t Have DRNG

## Slide 11: SPIRAL-Lite: For Constrained Responder Using Hash Certificate

## Slide 12: Responder Credential – Seed, Seed Password, and Touchstone
Credential | Seed | SP_3_4 | SP_3_3 | SP_3_2 | SP_3_1 | SP_2_4 | SP_2_3 | SP_2_2 | SP_2_1 | SP_1_4 | SP_1_3 | SP_1_2 | SP_1_1 | Touchstone
n | - | 3 | 3 | 3 | 3 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | -
m | - | 4 | 3 | 2 | 1 | 4 | 3 | 2 | 1 | 4 | 3 | 2 | 1 | -
Responder ROM passes | Not passes to FW | to n=3 responder FW |  |  |  | to n=2 responder FW |  |  |  | to n=1 responder FW |  |  |  | Public value signed by CA
Responder FW sends |  | to m=4 initiator FW | to m=3 initiator FW | to m=2 initiator FW | to m=1 initiator FW | to m=4 initiator FW | to m=3 initiator FW | to m=2 initiator FW | to m=1 initiator FW | to m=4 initiator FW | to m=3 initiator FW | to m=2 initiator FW | to m=1 initiator FW | to initiator
hash
hash
hash
hash
hash
hash
hash
hash
hash
hash
hash
hash
hash
Example for max responder SVN n = 3 and max Initiator SVN m = 4

## Slide 13: SPIRAL vs. USB Authentication Protocol
Property | SPIRAL | USB Auth Protocol | USB Auth Protocol w. shared secret
Asymmetric operation at every boot | No | Yes | No
Responder credential | May be X.509 or hash-based* | X.509 | X.509
Secure storage on responder | Not required | Not required | Required
* See SPIRAL-Lite slides and whitepaper.