## Slide 2
Connector Discussion
Paul Kappler
Network Hardware Engineer

## Slide 3: Possible Bi – Furcation Use cases
x16 Standard NIC
No Multi Host Capability
x16 Standard NIC
With Multi-Host Option
1 x16 or 2 x8
x16 Standard NIC
With Multi-Host Option
1 x16 or 2 x8 or 4x4
2 x16 Smart NIC
With Multi-Host Option
2 x16 or 4 x8
2 x16 Smart NIC
With Multi-Host Option
8 x4 or 4 x8
1x16 Single Host
1x16 Single Host w/Bi-Furcation
Dual Host
x16 Each
Quad Host
x8 Each
Quad Host
x4 Each
Host Use Cases
NIC Use Cases

## Slide 4: Proposed Bi-Furcation Scheme
 |  | Connector 0 & 1 (x16 option) |  |  | 
Network Card - Supported PCIe Configurations |  | 1 Host w/Bifurcation | 2 Hosts | 1 Host no bifuracton | 4 Hosts
 | System Bifurcation Setting --> | 1 x16 or 2 x8 or 4x4 | 2 x8 | 1 x16 or 1 x8 or 1x4 | 4 x4
 | System Encoding --> | 0b00 | 0b01 | 0b10 | 0b11
 | Add-in-Card Encoding |  |  |  | 
Card Not Present | 0b000 | - | - | - | -
Network Controller 1 x16 or 1 x8 or 1x4 or 1 Single 1 x16 EP that can reduce to x8 | 0b001 | 1 x16 | 1 x8 1 Host only | 1 x16 | 1 x4 1 Host only
Network Controller 1 x16 or 2 x8 Single 1x16 NIC that can bifurcate to 2 x8 | 0b010 | 1 x16 | 2 x8 | 1 x16 | 2x4 2 Hosts Only
Network Controller 2 x8 only Two 2 x8 Endpoints | 0b011 | 2 x8 | 2 x8 | 1 x8 1 Endpoint | 2x4 2 Hosts Only
Network Controller 4 x4 only Four 4 x4 endpoints | 0b100 | 4 x4 | 2x4 | 2x4 | 4 x4
Network Controller 1 x16, 2 x8, or 4 x4 | 0b101 | 1 x16 | 2 x8 | 1 x16 | 4 x4
RSVD | 0b110 |  |  |  | 
RSVD | 0b111 |  |  |  |