## Slide 1: OCP Mezz 3.0 Mechanical Recommendations
Andrew Junkins / Liang Long Chen / I Lang Cheng
2018-08-28

## Slide 2: Lenovo Position
Lenovo supports enumeration #14
  Weighing all pros/cons, this is best direction – but mechanical details are critical to broad adoption success
  Appears compatible with traditional rear IO general purpose server architectures.
    Lenovo has experience with similar solution in our Grantley ThinkServer systems: AnyFabric IO module
  Appears compatible with Scorpio architecture
Major Challenges/Concerns:
  Transceiver thermals – with constraints outlined on following pages, cage heat-sinks not feasible. Concern for rear IO applications
  EMI solution – space very limited to make robust seal

## Slide 3: Enum-14 Proposed Enhancement
Increase side KO width to 4.2 mm, both sides (see slide 4)
  Should these also be defined as ground pads?
Increase length to ~120 mm
  110 will be extremely challenging for NIC vendors
Avoid/minimize outriggers overhanging with chassis bulkhead/face-plate.
  To maximize MB beachfront availability
  Quarter-turn feasible? Wing-nut style touch-point?
  OEM neutral color for touch-points?
Connector - TBD
Require Mylar shield (or similar) to protect bottom side components during system installation/removal
  Will require KO for Mylar attachment points
  Needs to be thin, ~0.25-0.30 mm
Port LEDs should be included
  right angle LEDs and avoidance of light pipes preferred
RJ45 latches to be on top side of ports
A
C
B
D
E
F
G

## Slide 4: Guidance System: X-axis Assumptions
0.40~0.6 mm (nominal gap range)
3.5 mm
4.2 mm (PCB KO, both sides)
End View
NIC PCB
Module Guides – attached to MB, MB tray, or chassis
Feature to be symmetric

## Slide 5: PCBA Keep-out and Faceplate Constraints Proposals
＜ 12 mm (1U driven: cannot interfere with PCIe card keep out)
＜ 5.2 mm (1U driven: edge cannot extend below chassis base bottom surface)
PCB top side KO ＜ 10 mm (1U driven: rear wall flange clearance during installation/removal) Note this precludes port heat-sinks!
PCB bottom side KO ＜ 1.5 mm (1U driven: to clear chassis base during installation/removal)
PCB top surface
EMI/ESD solution need consideration between OCP rear bracket and chassis rear wall
H
I
K
J

## Slide 6: SR630 1U: rear wall x-section viewed from left
0
10.82
12.89-14.29
1.57
4.37
6.87
2.8
2.5
PCIe Card
Motherboard
Chassis bottom

## Slide 7: Enumeration 14 Dimensions – as delivered from FB
12.21mm
9.91mm
14.2mm
5.23mm
11.75mm

## Slide 8: Dual port QSFP
Bracket - Exterior
Bracket - Interior
Features to set gasket gap
Chassis EMI Gasket
Flange for stiffness,
1.0mm thk stock

## Slide 9: Quad port 10BaseT
Sink mount RJ45
Chassis EMI Gasket
Bracket - Exterior
Bracket - Interior
Features to set gasket gap
Flange for stiffness,
1.0mm thk stock

## Slide 10: 10BaseT – EMI Gasket Interface
1.25mm
1.65mm
EMI surface overlap
EMI Gasket –
Apply to chassis
Side View
X-sections
EMI sealing is a concern – lack of robust interface

## Slide 11: QSFP – EMI Gasket Interface
1.65mm
Overlap from tangent of bend line
EMI surface overlap
Side View
X-sections
EMI Gasket –
Apply to chassis
EMI sealing is a concern – lack of robust interface

## Slide 12: Back Up

## Slide 13: SR630 1U: Rear Wall Construction X-section View
Rear wall (bottom side)
Rear wall bar
Planar PCB
Chassis base (top side)
Rear wall (bottom side)

## Slide 14: SR630 1U: rear wall x-section viewed from front
LP PCB
LP PCB
LP PCB
Rear wall bar
10.8mm
Planar PCB
12.9mm
LP Bottom KO
LP Top KO
LP Bottom KO
12.7mm
Chassis base
Rear wall
2.8mm
14.3mm

## Slide 15: ThinkServer RD550 1U: Rear View with AnyFabric
AnyFabric: x8 PCIe module with rear installation, blind-mate to Mb
AnyFabric modules