## Slide 1: Comments on OCP Mezz v3 & Connector/Pinout Proposal
Rev 01
8/16/2017
Mike Witkowski, Paul Chuang, Bao Chen, Alex Kuo
Send comments/questions to mike.witkowski@hpe.com

## Slide 2: Agenda
Brief comments on Options #13 and #14
Proposal for connector/pinout for OCP Mezz v3 (works with Options #13 and #14)
Other questions HPE would like OCP Mezz community to consider

## Slide 3: Comments on Options #13 & #14

## Slide 4: Comments on Options #13 and #14
HPE supports Option #14 as the primary option for OCP with the following caveats:
  Because the large form factor uses width for expansion, this model not aligned with majority of our platforms
    Size of the cut out, impact to signal routing, impact to component placement, etc.
  Thus, our adoption might be limited to only the small form factor version of Option #14
    Still under investigation, depends on final dimensions of large form factor adopted by OCP Mezz community
    Looking at possible ways of mounting large Option #14 cards in different locations/orientations (vertical/horizontal)
Another option to consider is to merge Option #13 with proposed PCIe CEM Alternative
  Several PCI SIG members are in process of proposing PCIe CEM alternative for PCIe Gen 4, 5, and beyond
  Uses SNIA SFF TA-1002 instead of existing PCIe CEM (improved mechanical and electrical properties)
  Propose using extra set of pins for OCP Mezz specific signals and make compatible with PCIe CEM Alternative
  Supports ability to build slight modification of PCIe CEM Alt cards to enable them to act as OCP Mezz cards
  Primarily to support large form factor, high power OCP Mezz applications

## Slide 5: OCP Mezz 3.0 Connector/Pin-out Proposal

## Slide 6: Goals and Attributes of this Proposal
Support higher data rates (at least up to 112 GT/s)
Excellent electrical performance
Edge card connector with multiple mounting options
  Vertical, co-planar (straddle mount), right angle
  Cabled and optical options are a big bonus
Small, high pin density connector
  More flexible placement, better/shorter signal routes
Supports OCP Mezz 3.0 Options #13 and #14
Connector compatibility with other industry standards
  SNIA SFF TA-1002 (supports EDSFF, Gen-Z, and proposed PCIe CEM alternative)
  Possible future SFF-8639 follow-on connector for drives

## Slide 7: SFF TA-1002
  Currently specifies vertical and right angle connectors
  Three lengths: 4x lane pairs, x8 lane pairs, x16 lane pairs
  Up to 112 GT/s
  In process of adding co-planar straddle mount connector
Copyright © 2017 SNIA. All Rights Reserved

## Slide 8: SFF TA-1002
  Current proposed pinouts for Gen-Z and PCIe CEM alternative
  EDSFF is similar but has not been publicly published yet

## Slide 9: OCP Mezz Connector/Pinout Proposal
Enhance SFF TA 1022 to support OCP Mezz
  Specify an additional 28 pin section for additional OCP Mezz requirements
  Add this section for the x8 and x16 versions (could also support x4)
  These would be specified as options 3C (for x8) and 5C (for x16)
  The editor/chair of SFF TA-1002 is ready to make these changes for OCP
Place the OCP Mezz section to enable PCIe CEM Alt compatible slots
  OCP Mezz placed at the “front end” of the connector
  Supports OCP Mezz Option #14
  But also enables slight modification to PCIe CEM alternative to enable Option #13 in systems/solutions that require it (i.e. large form factor OCP Mezz)
  PCIe CEM Alt slots can accommodate Option #13 OCP cards (w/o OCP support)
  Option #13 slots can accommodate PCI CEM Alt cards (w/o OCP support)

## Slide 10: Proposed OCP Pinout
  OCP Mezz is identical to PCIe CEM alternative, except with additional 28 pin section at the beginning of connector

## Slide 11: OCP Mezz 3.0 Additional questions to consider

## Slide 12: Separate REFCLK with Independent SSC (SRIS) vs. Common REFCLK Rx
Existing PCIe specification generally states the following
  Support for common REFCLKs are mandatory
  Support for SRIS is optional
With the dawn of PCIe Gen 4 and 5, some members of the SIG would like to consider the following:
  Support for SRIS is mandatory
  Support for common REFCLKs is optional
Why?
  Reduce the number of pins on the connectors (especially multi-host, socket direct functionality)
We need to understand the capabilities of current devices
  Root Ports
    We understand that most high volume devices with root ports already support SRIS, correct?
  End Points
    What is the current state of the art in regards to SRIS support in end points?

## Slide 13: Questions/Issues?

## Slide 14: Thank You