## Slide 2
SERVER
OCP NIC Community Update April 2022 Sub-group Project wiki: https://www.opencompute.org/wiki/Server/Mezz
Mailing List: https://ocp-all.groups.io/g/OCP-NIC
NIC3.0

## Slide 3: Agenda
OCP Tech Week 2022
SI Test Fixture Update
Thermal Test Fixture Update
PCIe Gen6 connector analysis
NCSI OOB landscape

## Slide 4: OCP Tech Week 2022
OCP Foundation Month-long Tech Week workshop
2-days for Server Workgroup and its sub-groups on
  4/26 (Day 1): OCP NIC, OAI, HPC & ODSA
  4/27 (Day 2): Modularity standardization, DC-MHS, DC-SCM 2.0
  8.30am to 11.30am PT
Registration:
  https://www.eventbrite.com/e/ocp-tech-talks-server-sessions-1-2-april-26-27-830-1130ampt-registration-277678081617
  https://tinyurl.com/ocptechweek2022

## Slide 5: OCP Tech Week 2022
OCP NIC presentation:
  OCP NIC Next-Gen Trends
      Speeds, Form Factor
  Thermal Test Fixture PCIe Gen5 support (tentative)
  ?
  ?

## Slide 6: SI PCIe Gen5 test fixture update
CLB Gen5 status:
  Gerbered in January
  PCB arrived at assembler mid-March
  Assembled units arrived end-of-March
  Preliminary results ~ mid-April
CBB Gen 5 Status:
  Based on Gen4 design
  Updates to align with PCI CEM
  To be staffed within Dell
Netlist block diagram
OCP3 SFF CLB Gen5 ECAD
Calibration
CLB board 1
Impedance Coupon
CLB board 2
Presenter: Jason Rock (Dell)

## Slide 7: PCIe Gen5 thermal test fixture update
Much of the existing TTF can be re-used based on simulation *
  Mechanicals not impacted
  PCB designed to support PCIe Gen5
  * PCIE-C (cable assembly) must be rated and sourced for PCIe Gen5 lane speed
  Lab experimentation required to confirm simulation
OCP NIC 3.0 TTF in use
Example cable assembly from Samtec
* Image sourced from Samtec
Presenter: Jason Rock (Dell)

## Slide 8
SERVER
SNIA SFF TA-1002 Connector SI Requirements For OCP NIC 3.0 PCIe6 Speed
NIC3.0
Amphenol
Presenter: Zhineng Fan (Amphenol)

## Slide 9: Background
OCP NIC start looking at PCIe6 64G PAM4 speed
NIC interface connector follows SNIA SFF TA-1002 spec
    SNIA SFF TA-1002 did not specify 64G PAM4 connector SI requirements
    SNIA SFF TA-1002 specified 56G PAM4, 32G NRZ, 56G NRZ and 112G PAM4
Presenter: Zhineng Fan (Amphenol)

## Slide 10: SNIA SFF TA-1002 Connector SI Requirements
Return loss is the same for all speed
Presenter: Zhineng Fan (Amphenol)

## Slide 11: Insertion Loss and Xtalk
56G PAM4 and 32G NRZ share the same limit line
56G NRZ and 112G PAM4 share the same limit line
Presenter: Zhineng Fan (Amphenol)

## Slide 12: NCSI sideband landscape
RMII
7 parallel pins
Not backward compatible
RGMII
12 parallel pins
Not backward compatible with RMII
SFF
2 spare RFU pins available
NIC ASIC
Is NIC ASICs capable of RGMII?

## Slide 13: Discussion bin list
DMTF NIC self-shutdown recommendation
Elegant cable-up solution
    Zion uses 4C+ vertical connector to 4C+ saddle mount connector cable
1G NCSI/RGMII side-band support
PCIe Gen6 support
    PCI-SIG spec at rev1.0*
    800G Ethernet port
    Additional side-band

## Slide 15: Gather feedback throughout the year
Provide your feedback at: https://tinyurl.com/feedback2ocpnic

## Slide 16: Thermal Test: TSFF TTF Status
Mechanical files received. Pending mechanical engineer peer review
Uses existing TTF with 3 different components to convert to TSFF.

## Slide 17: NIC self-shutdown discussion
Get DMTF & HW management feedback
Discussion 1: NIC self shutdown as optional feature?
Discussion 2: NIC self shutdown as threshold?
Discussion 3: If NIC self shutdown implemented, it shall provide mechanism to enable/disable the feature?

## Slide 18: NIC self-shutdown discussion
Discussion 1:
NIC self shutdown as optional feature
Keep as optional

## Slide 19: NIC self-shutdown discussion
Discussion 2:
NIC self shutdown as threshold
Current recommendation
Change between to “at least”
Or remove this recommendation

## Slide 20: NIC self-shutdown discussion
Discussion 3:
If NIC self shutdown implemented, it shall provide mechanism to enable/disable the feature