## Slide 2
OpenDCRE
Next-Generation Data Center Management
Andrew Cencini & Steven White
VP Engineering / Chief Architect
Vapor IO

## Slide 3: Agenda
Overview & Motivation
Hardware
Software
Features
Demo

## Slide 4: OpenDCRE – Overview
OpenDCRE: Open Data Center Runtime Environment.
Combination of open-source hardware and software for out of band data center telemetry and management.
Built by Vapor IO and contributed to the community.
Multiple form factors and broad vendor support.
Modern, flexible, easy-to-use.
Uses power line and/or LAN as communications channels

## Slide 5: OpenDCRE - Motivation
Out-of-Band Management (IPMI) is painful
  Legacy binary protocol (IPMI 1.0: 1998)
  Complex and opaque (IPMI 2.0 Spec, 644 pages)
  Varied tool support
  Requires BMC (Baseboard Management Controller)
  Requires OOB Switch, Cabling
OpenDCRE is not painful!
  Securable, GPLv2 RESTful API, hardware and
  Linux Distribution for data center management.
  NO BMC, TOR Switch, Cabling (PLC Comms)
IPMI 2.0 Specification, Intel (2013)

## Slide 6: OpenDCRE - Motivation
The world runs on REST
DevOps tasks tend to fall into the same broad categories
  Sensor reading
  Power control
  Inventory/Provisioning
OCP OpenRack bus bar makes for great communications channel
Related work:
  Redfish (HP)
  OpenBMC (Facebook)
http://i.imgur.com/o0lb2ek.jpg

## Slide 7: OpenDCRE - Software
OpenDCRE
  Runs as Docker container on OpenMistOS
  Serial Communications via GPIO to HAT
  HAT uses PLC to communicate with device bus
  REST Endpoint for interacting with bus:
    Scan, read sensors, power control, etc.
    Can drop in TLS Certs for SSL, integrate with OAuth via config as well (Nginx/uwsgi)
  Emulator included for evaluation w/o HW
    Configurable (JSON), automatically runs in absence of HAT
  GPLv2, integrated into OMOS.

## Slide 8: OpenDCRE – API/Features
  Version: Get HW/API/SW version
  Scan: Enumerate items connected to the bus
  Read: Read and interpret a given sensor or device attached to bus
    Temperature, humidity, fan speed, power consumption
  Power: Turn power on, off, cycle, and get status
    Voltage, current, on/off, over/under voltage/current
  Asset: Asset and hardware information
  Boot Target: Set/get boot target for PXE/HDD boot for provisioning, etc.
  LED: Toggle chassis LED for visual location/verification, remote service
  Fan: Control fan speed

## Slide 9: OpenDCRE REST API Examples
https://host:port/opendcre/1.2/power/1/1[/{on|off|cycle|shutdown|status}]
https://host:port/opendcre/1.2/read/thermistor/1/2
https://host:port/opendcre/1.2/asset/1/5
https://host:port/opendcre/1.2/led/1/7[/{on|off}]
https://host:port/opendcre/1.2/fan_speed[/speed_rpm]

## Slide 10: OpenDCRE – The Gateway Drug…
OpenDCRE v1.2 – IPMI 1.5/2.0 Support
  All features of OpenDCRE
  Auth: None, Password, MD2, MD5, RAKP_HMAC_SHA1
  Integrity: None, HMAC_SHA1_96
  Encryption: None, AES_CBC_128
  Virtually unlimited #BMCs from single OpenDCRE endpoint
Redfish & OpenBMC support coming soon
http://sr.photos3.fotosearch.com/bthumb/CSP/CSP991/k12456743.jpg

## Slide 11: OpenDCRE - Hardware
Raspberry Pi 2 Model B
OpenDCRE HAT Board
Power-Line Communications (PLC)
Sensors/Devices
  Temperature (thermistor)
  Power Control (OCP)
  Other hardware – fans, LED, etc.
Open-Source HW (OCP)

## Slide 12: Power Line Communications
  Based on Yamar SIG60
  Tightly integrated design
  Two frequency choices
  Optimized for noisy 12VDC automotive environments
  Simple control through a UART connection with 4 additional GPIO
  Low power with sleep capability

## Slide 13: PCB Layout
Pi HAT (Hardware Attached on Top) compliant form factor
EEPROM for identification and auto-configuration in the operating system
Simple 2 layer layout
Only top side components
Connections for RS232 and SMBus
Switching between PLC and onboard microcontroller for firmware development
Powered completely from 12VDC

## Slide 14: OpenDCRE - Demo

## Slide 15: Future
OpenDCRE 1.2 Release – March 10, 2016
Community contributions – additional device types, sensors, etc.
Additional form factors to be announced
OpenMistOS for Raspberry Pi – wheezy to jessie migration.
Docker-compose support.
Additional integrations (OpenStack, etc.).
Further support for 19” environments, Redfish, OpenBMC.
GitHub: https://github.com/vapor-ware/opendcre

## Slide 16: Thank You
Questions?
Contact:
  Andrew Cencini
  andrew@vapor.io
  Steven White
  steven@vapor.io

## Slide 17
Thank You