## Slide 1
How SPIRAL Boosts Crypto of Authentication and Attestation by Over 20,000 Times
Xiaoyu Ruan and Will Stevens
{xiaoyu.ruan; william.a.stevens}@intel.com
For OCP security forum
March 5, 2019

## Slide 2: Problem Statement
The authentication and attestation protocol (designed based on USB Type-C protocol) is not optimized for performance.
On constrained devices, running the protocol takes a long time during boot.
For many environments, boot performance is critical.
 | Legacy | Pre-Shared-Key | SPIRAL
Boot speed | Slow | Fast | Fast
Secure non-volatile storage required on attestor device | Not Required | Required | Not Required
Problem
Solutions
Pre-shared key: Platform and Attestor Device both save pre-shared key.
SPIRAL

## Slide 3: Legacy Protocol: Heavy Crypto (Asymmetric-Key) Every Boot
Attestation of Systems and System Components *DRAFT*
11.6. Authentication, Attestation, and Enrollment protocol
Requires asymmetric-key operations. Authentication of all attestor devices could take a long time.
Asymmetric-key operation is slow on constrained attestor devices.
Amount of data transmitted in “challenge Response” is big and slow on slow buses (e.g., I2C).

## Slide 4: SPIRAL: Light Crypto (Symmetric-Key Only) Every Boot

## Slide 5: Performance Comparison: Speeding up Crypto Operations by over 20,000x
On Intel CSME (converged security and management engine), 200MHz
Algorithm | Performance
ECDSA P256 sign | 9.3 ms
ECDSA P256 verify | 8.0 ms
RSA 2048-bit sign | 16 ms
RSA 2048-bit verify | 2.0 ms
HMAC-SHA256 | 186 Mbytes/s
AES-128 | 267 Mbytes/s
Legacy protocol | ~17.3 ms (ECDSA) / 18 ms (RSA)
SPIRAL | ~0.8 μs (>20,000 times faster)
32 bytes smaller than ECDSA/ECDH
224 bytes smaller than RSA
SPEED
Data Transmission

## Slide 6
Include in next revision of Cerberus as an option for authentication and attestation?
  Intel is in the process of implementing Cerberus AC-RoT in several devices.
Incorporate in spec of Attestation of Systems and System Components?
What’s Next?

## Slide 7: Backup

## Slide 8: SPIRAL-OneWay : Initiator Authenticates Responder
See Backup for flow when responder does not have DRNG

## Slide 9: SPIRAL-TwoWay: Mutual Authentication
Responder is required to have DRNG in order to authenticate initiator.

## Slide 10: SPIRAL-OneWay : When Responder Doesn’t Have DRNG