## Slide 2
SERVER
OCP NIC Community Update July 2022
For Server Workgroup Sub-group Project wiki: https://www.opencompute.org/wiki/Server/Mezz
Mailing List: https://ocp-all.groups.io/g/OCP-NIC
NIC3.0

## Slide 3: Agenda
OCP Global Summit 2022
SI Test Fixture Update
Thermal Test Fixture Update

## Slide 4: OCP Global Summit 2022
There are 6 abstracts related to NIC has been tentatively accepted for presentation.
Final decision to be made after reviewing presentation materials
ID | Title
2841 | OCP NIC 3.0 Design Specification Update
2788 | Leveraging Existing OCP NIC Interconnect for PCIe Gen 6 Architectures.
2617 | OCP NIC 3.0: Present and The Future
2683 | Advanced thermal testing and characterization for pluggable IO
2705 | New TSFF test fixture airflow measurements and definitions
2783 | SmartNIC & OCP NIC-3 in Modular Hardware Systems (DC-MHS)

## Slide 5: PCIe® 5.0 SI Test Fixtures
CLB 5.0 32GT/s status:
  First proto start from 4.0 design
  Dell & Tektronix testing reveal impedance / return loss issue
    Root cause: manually-placed connector anti-pads from 4.0 design present in 5.0 design
  ECAD to complete this week:
    Anti-pads removed
    Additional trace tuning to mitigate additional discontinuities based on measured data
CBB 5.0 32GT/s status:
  Start from 4.0 design
  Updates to align with PCI-SIG®
  Routing starts once CLB verified
OCP NIC 3.0 SFF CLB 5.0 prototype
Calibration
CLB board 1
Impedance Coupon
CLB board 2

## Slide 6
The TTF was designed to support speeds up to PCIe® 5.0 32GT/s
  Uses very low-loss material
Cable assembly must be updated for 32GT/s signaling transmission
  Received 1 of 2 cable assemblies
  Lab experimentation requires NIC 3.0 PCIE Gen5 unit
PCIe® 5.0 Thermal Test Fixture (TTF)
OCP NIC 3.0 TTF in use
Example cable assembly from Samtec
Request for a contributor to supply a Gen5 card for validation

## Slide 8: Gather feedback throughout the year
Provide your feedback at: https://tinyurl.com/feedback2ocpnic