## Slide 2: OCP NIC Community Update for Server Workgroup August 2020 OCP NIC Subgroup Sub-group Project wiki: https://www.opencompute.org/wiki/Server/Mezz Mailing List: https://ocp-all.groups.io/g/OCP-NIC
Server Workgroup

## Slide 3: Agenda
Revamped Mezz Wiki
OCP Tech Week
Signal Integrity Update
Mechanical update
Specification update
Taller SFF

## Slide 4: Revamped wiki
Release Candidate for Public Review
Official Release Spec
Collaterals
Fixture Design Files
Fixture for Purchase

## Slide 5: Revamped wiki

## Slide 6: OCP Tech Week
Dates: Nov 9-10; Nov 12-13
NIC track in Tuesday Nov10 8am-12pm (PST)
Submission deadline Sept 9 (in 2 weeks)

## Slide 7: Signal Integrity Update
SI workgroup recommends NIC Insertion Loss parameters for PCIe Gen5 as below:
    SFF: -7.0dB @ 16GHz
    LFF: -9.5dB @ 16GHz
As reference, PCIe CEM insertion loss is -9.5dB @ 16GHz
Next step, review in NIC sub-group monthly meeting then open for 2 weeks public review / feedback
DRAFT

## Slide 8: Mechanical Update
Initial mechanical compliance fixture 3D as below
Feedback from NIC sub-group to use 4C & 4C+ connector for mating
Fixture would be able to check X, Y & Z critical dimensions
Fixture would be transparent for easy identification of UUT interference (if any)

## Slide 9: Specification update
Rev1.01 draft still under contributor review.
    Discussion from NIC working session conclude changes around 12V_Edge being optionally OFF during ID_mode & Programming_mode needs additional validation data from multiple NIC vendors
Plan to close within contributors early next month in September NIC working session

## Slide 10: Taller SFF
With NIC3.0 SFF extending to support PCIe Gen5, x16 lanes is enough to drive 400Gb line rate
NIC3.0 dimension today unable to support OSFP or adequately cool QSFP-DD due to Z-height restrictions
As announced during OCP global summit, NIC sub-group would investigate taller SFF.
We will be starting this work in next week’s working session

## Slide 12
March 4-5, 2020