## Slide 2: OCP NIC Community Update December 2019 OCP NIC Subgroup Sub-group Project wiki: https://www.opencompute.org/wiki/Server/Mezz Mailing List: https://ocp-all.groups.io/g/OCP-NIC
Server Workgroup

## Slide 3: Agenda
Change overview and schedule (0v92 1v00)
Compliance Program
Signal Integrity budget work for post 1v00
Global summit workshop abstracts
OCP Experience Lab

## Slide 4: November 2019 F2F working session
Hosted by Dell EMC @ Round Rock (Austin, Texas)
Representatives from: Amphenol, Broadcom, Dell, Facebook, Hewlett Packard Enterprise, Intel, Marvell, Mellanox, TE Connectivity, University of New Hampshire

## Slide 5: Specification Update (0v92)
Draft 0v92 posted on the OCP Wiki site
Request for comments phase closed 11/22
Key changes
Section 3.10 – Clarified RBT hotswap not supported in DSP0222 1.1/1.2. Future revision of DSP0222 required.
Section 3.11 – Max timing between AUX_PWR_EN/MAIN_PWR_EN and NIC_PWR_GOOD change from 25ms to 50ms
Section 4.10.3 – Changed FRU offset 3 to show FRU record version released with version x.xx. Compatible FRU contents use the latest field. This prevents having to revise the field when no FRU changes have been made.
Section 7.1.x – Add text for co-reporting EN55024 + EN55035
Minor text updates (no technical content change)

## Slide 6: Specification Update – Path to 1v00!
Known changes and additions for Version 1v00
Section 2.x – Mechanical group working on finalizing CTF dimensions
Section 3.4.5 – Multiplex secondary connector PRSNTB[3:0] pins on scan chain thermal (TEMP_WARN, TEMP_CRIT, FAN_ON_AUX) and WAKE_N for LFF implementations
Section 4.3 – Add second Management Controller MAC address algorithm (Label example #4)
Minor text updates (no technical content change)
Release Schedule
December 4th-6th – update mechanical drawings; send to ME team for review
December 9th – send 0v99 draft out to the OCP-NIC and OCP-Server distribution lists for two week RFC period
December 20th – release specification as 1v00 if there are no further comments

## Slide 7: 1v00 Release Package Contents
OCP NIC 3.0 Specification (PDF)
Mechanical
    2D mechanical drawings (PDF)
    3D models (STEP)
Thermal
    Thermal CFD models (Icepack)
    Thermal Test Fixture (brd/STEP)
PCIe CLB/CBB for Gen3/Gen4 (brd)
Shock and Vibe fixture (Parasolid)
SFF/LFF example block diagrams (PDF)
Pinout table (spreadsheet)
PCIe bifurcation decoders (spreadsheet)
MC MAC address Provisioning Calculators (spreadsheet)
Example FRU (Spreadsheet/HEX)

## Slide 8: Specification Collateral
Updated
New Doc
https://www.opencompute.org/wiki/Server/Mezz#Updated_Specification_Docs

## Slide 9: UNH-IOL Compliance Program
Dell-EMC developed OCP NIC 3.0 PCIe Gen3/4 test fixtures
UNH-IOL is setting up the test fixture program
Link and Contact: https://www.iol.unh.edu/solutions/test-tools/ocp-pcie

## Slide 10: PCIe Gen5 on OCP NIC 3.0
OCP NIC 3.0 has provision for PCIe Gen5 during connector selection
Current spec covers Gen4 and follows CEM spec for insertion loss budgeting after discussion
Gen5 is supported by connector. Similar definition need to be in place. SI workgroup is working on this topic.
If you are interested to join this work, please reach out to Samit Ashdhir ashdhir@fb.com

## Slide 11: 2020 OCP Global Summit
March 4-5, 2020 @ San Jose Convention Center
Known topic submittals for the OCP NIC 3.0 Track (under review):
The journey to OCP NIC3.0 v1.0 and beyond
Present our development effort from the initial drafts to version 1.00. Share recent spec updates, focus areas and discuss development for post 1.00
OCP NIC 3.0 Specification Ratification Process
  Discuss updated specification release process and inclusion of a request for comments phase and how we better inform the OCP NIC 3.0 community.
https://www.opencompute.org/summit/

## Slide 12: OCP Experience Lab
Returning for 2020!
Interact with members of the OCP community
Showcase for OCP NIC 3.0 hardware
Live and static demos
Point of Contacts
April Fisher april.e.fisher@intel.com
Elad Wind elad@mellanox.com
https://www.opencompute.org/summit/global-summit/ocp-experience-lab

## Slide 13
Q&A