## Slide 1: OCP NIC 3.0 Discussion
Rev 10
9/20/2017
Jia Ning, Hardware Engineer, Facebook
Yueming Li / John Fernandes, Thermal Engineer, Facebook
Joshua Held, Mechanical Engineer, Facebook
Updated
New

## Slide 2
Understand the problem
  Collect feedback from Internal, NIC vendors, system vendors, CSP
  Talk to NIC and system vendors to understand use cases
  Target to unblock new use cases and thermal challenge, with migration challenge considered
Find and implement a solution
  Work on NIC form factor change proposal under OCP Mezz NIC subgroup
  Form consensus in work group and finalize specification change and migration plan
  Leave enough time to impact the planning for next generation NICs cards and systems
OCP NIC 3.0 General Approach

## Slide 3: Snapshot of milestones :

## Slide 4: 9/25 workshop @ Dallas, TX
1:30-1:50 | 20 min | Welcome and General update | Bill Carter - CTO, OCP Archna Haylock - Community Director, OCP
1:50-2:30 | 40 min | Project Olympus update | Mark Shaw, Microsoft
2:30-2:40 | 10 min | Break / buffer | 
2:40-2:50 | 10 min | Overview of OCP NIC 3.0 status | Jia Ning, Facebook
2:50-3:00 | 10 min | Mezz 3.0 Specification - Thermal considerations | John Fernandes and Yueming Li, Facebook
3:00-3:10 | 10 min | Mezz 3.0 Specification - Mechanical update | Joshua Held, Facebook
3:10-3:20 | 10 min | Mock-up review and demo | Joshua Held, Facebook
3:20 – 3:30 | 10 min | Break / buffer | 
3:30 – 3:45 | 15 min | Connector Update | TE
3:45-4:00 | 15 min | Connector Update | Amphenol
4:00 – 4:20 | 20 min | Dell – EMC update | Jon Lewis, Dell-EMC
4:20 – 4:30 | 10 min | Break / buffer | 
4:30 – 5:00 | 30min | Pinout discussion | Jia Ning, Facebook
5-5:30 | 30min | NIC Management | Hemal Shah, Broadcom
Updated Agenda
Start: 1:30PM End: 5:30PM State Room
http://dcd.events/conferences/colo-cloud/benefits/engineering-workshops

## Slide 5
 | Description of change made to Mezz 2.0 | Status | Summary of Feedback | 2.0 Compatibility
14 | Straddle Mount / RA at rear; Expend towards the side | Open | Confirmed on 9/20 as only option for OCP NIC 3.0 Got most support from NIC / System / Connector suppliers More details to be worked out | No
Summary of Open Options
Updated

## Slide 6
 | Description of change made to Mezz 2.0 | Status | Feedback | 2.0 Compatibility
1 | Add 16mm stacking height option | Close | NIC placement challenge has no improvement | Yes
2 | Extend width | Close | NIC placement challenge has no improvement | Yes
3 | Extend length | Close | NIC Placement challenge is partially addressed NIC PCIe routing challenge still exist | Yes
4 | Move connector B to right edge | Close | NIC PCIe routing challenge gets worse | Partial
5 | Flip ASIC to top | Close | Force tradeoff between system configuration flexibility and thermal | Yes
6 | Move connector A to the left edge and keep same Y-location as Mezz 2.0 | Close | NIC PCIe layout has crossing Possible backward compatibility for x8 | Partial
7 | Move connector A to the left edge with smooth PCIe lane sequence | Close | Lack of backward compatibility Most challenging for migration Being used in Simulation in June/July | No
8 | Based on 7 and turn connector B by 180º | Close | NIC PCIe layout has crossing Possible backward compatibility for x16 with dual layout | Partial
9 | 2x Mezz 2.0 footprint side by side | Close | Limited thermal improvement due to connector placement | Yes
10 | RA PCIe connector at side | Close | Stacking prevents 1U system to fit 1x Mezz + 1 PCIe CEM | No
11 | Co-planner/ straddle Mount connector at rear | Close | Major pros (thermal and servicing) and cons(large cutout, needs extension for small card) identified | No
12 | Right Angle Connector at rear | Close | Thermal concern of RA connector dams the air flow Stacking prevents 1U system to fit 1x Mezz + 1 PCIe CEM | No
13 | Co-Planner / Straddle Mount Connector at side | Close | New option; Major pros (thermal) and cons(large cutout) identified | No
Summary of Closed Options
Updated

## Slide 7
Impact to NIC | Priority
Use case – higher Thermal | High
Use case - Larger IC package | Medium
Use case - Multi-chip card | Medium
Use case - IC w/ DRAM | Medium
Stable form factor considering needs in the next 5 years | High
Impact to system | 
Feasibility for New System mechanical and board design | High
Feasibility to migrate existing system mechanical design to support OCP NIC 3.0 | Medium
Feasibility to migrate exist board design to support OCP NIC 3.0 | Low
Impact to ecosystem migration | 
Existing baseboard to support OCP NIC 3.0 | Low
Plan to allow system and card to migrate to OCP NIC 3.0 | High
OCP NIC 3.0 Migration Community Feedback

## Slide 8
Straddle Mount/RA – interface at back
Enumeration of #14
Option 14
Pros:
Thermal / Mechanical
  Flexible heatsink height definition
  Eliminated the complex, and discrete stacking height tradeoff
  Better thermal performance for both ASIC facing up and added width
  Friendly on EMI design and servicing
  For baseboard not able to make cut out, it may design in the RA connector to take same OCP NIC 3.0
SI potential / form factor stability
  In general edge card connector has more potential compare to Mezz style
  Target to accommodate 32Gbps NRZ for connector candidate
  Connector info is pending for connector suppliers’ clearance to publish
Hot service potential
W1 and W2 Discussion see following pages
Side Views
Straddle
Mount
Right
Angle
Baseboard
w/ cutout
Baseboard
w/o cutout

## Slide 9
#14 Cut out size analysis
Enumeration of #14
Propose 1 | 
W1 | ~78mm [3.07”]
W2 | ~ 2x W1 + some overhead
L | 110mm [4.33”]
Propose 2* | 
W1 | ~68mm [2.67”]
W2 | ~ 2x W1 + some overhead
L | 110mm [4.33”]
* Do not plan to define 2x different W1
Option 14
Side Views
Straddle
Mount
Right
Angle
Baseboard
w/ cutout
Baseboard
w/o cutout
Propose 3* | 
W1 | 74mm
W2 | 118mm
L | 110mm
Updated
Propose 4* | 
W1 | 74mm
W2 | 118mm
L | 115mm

## Slide 10
Enumeration of #14
Updated
Discussion:
The size of the module is the subject of discussion
Overall it’s a tradeoff between system and NIC
We proposes 2x sizes to be evaluated first based on Mezz 2.0 size / I/O size / Connector Size
  W1= 68mm L= 110 mm
  W1= 78mm L= 110 mm
  W1= 74mm L= 115 mm
  W2= 118mm L= 115 mm
    Undergoing Discussion to increase W1/W2 by 2mm
Refer to mechanical discussion v02 for detail
Straddle Mount/RA – interface at back
Option 14
Side Views
Straddle
Mount
Right
Angle
Baseboard
w/ cutout
Baseboard
w/o cutout

## Slide 11
Enumeration of #14
Updated
Specific Discussion points with NIC suppliers
Feasibility of fitting NIC without DRAM into[W1=74mm, L=115mm]
Feasibility of fitting NIC with DRAM into [W2=118, L=115mm]
Undergoing Discussion to increase W1/W2 by 2mm
Feasibility of keeping card thickness to 62mil +/-10% ?
Feasibility of reducing bottom side placement clearance from 2.9mm to lower (max 2.25) mm; PCIe CEM=2.67mm as reference. This is to support baseboard with an existing RA style connector
  2x out of 2x NIC suppliers shows difficult with supporting <2.25mm
  Next step=> Follow up with Connector Suppliers to enable TA-1002 RA style with added offset
Anything the specification can do differently to reduce peripheral components?
Straddle Mount/RA – interface at back
Option 14
Side Views
Straddle
Mount
Right
Angle
Baseboard
w/ cutout
Baseboard
w/o cutout

## Slide 12
Enumeration of #14
Updated
Specific Discussion points with system suppliers
Feasibility, and impact of having cut off [W1=74mm, L=115mm] on baseboard/system
Feasibility of supporting [W1=118mm, L=115mm] module on full width board/system
Size above is card size; consider overhead for mechanical implementation and useable baseboard area. Detail refer to mechanical discussion v02
Feasibility of limiting baseboard thickness to 3x options: 62mil / 76mil / 93mil /120mil (requested by one system supplier)
Z-height utilization analysis of Straddle mount and RA cases on typical system configuration
  Assuming ASIC + Heat sink max height =11.5mm
Straddle Mount/RA – interface at back
Option 14
Side Views
Straddle
Mount
Right
Angle
Baseboard
w/ cutout
Baseboard
w/o cutout

## Slide 13
Connector Definition and Enabling 1
Enumeration of #14
Connector candidate is based on SFF-TA-1002
https://ta.snia.org/higherlogic/ws/public/download/1137/SFF-TA-1002%20Specification%20Multi%20Lane%20High%20Speed%20Connector%200.0.9.pdf
Option 14
 | Connector | Description
Connector A | “4C” style of TA-1002 + 28 circuits OCP NIC sideband bay Total 168 circuits | 16 PCIe + clock + Power +MISC + NC-SI
Connector B | “2C” style of TA-1002 Total 84 circuits | x8 PCIe + clock + Power +MISC
Connector A
Conn B
Style | RA/SM | Baseboard Thickness | Circuit Count | Notes – based on SFF-TA-1002
RA1-168 | Right Angle | N/A | 168 | Adjust Right angle offset from center of add on card to top surface of baseboard from 3.05mm to 3.80mm Add one extra 28 circuit bay
RA1-84 | Right Angle | N/A | 84 | Adjust Right angle offset from center of add on card to top surface of baseboard from 3.05mm to 3.80mm
SM1-168 | Straddle Mount | 62mil +/-10% | 168 | Base on 4C, Add one extra 28 circuit bay
SM1-84 | Straddle Mount | 62mil +/-10% | 84 | Straddle Mount of SFF-TA-1002 2C
SM2-168 | Straddle Mount | 76mil +/-10% | 168 | Base on 4C, Add one extra 28 circuit bay
SM2-84 | Straddle Mount | 76mil +/-10% | 84 | Straddle Mount of SFF-TA-1002 2C
SM3-168 | Straddle Mount | 93mil +/-10% | 168 | Base on 4C, Add one extra 28 circuit bay
SM3-84 | Straddle Mount | 93mil +/-10% | 84 | Straddle Mount of SFF-TA-1002 2C
SM4 | Straddle Mount | 120mil +/-10% | 168/84 | Request SI and feasibility study only
*Expect 168 circuits being more common
Preliminary; under discussion in OCP NIC subgroup
Updated

## Slide 14
Enumeration of #14
Connector candidate is based on SFF-TA-1002
https://ta.snia.org/higherlogic/ws/public/download/1137/SFF-TA-1002%20Specification%20Multi%20Lane%20High%20Speed%20Connector%200.0.9.pdf
Connector A
Conn B
Next steps:
Pinout
  Work with community members to define pinout
  Work with system suppliers to find out enabling priority and schedule requirement
  Discussion points:
    Power domain (do we want to keep both P12V and P12V Aux)
    Additional pins
Connector Enabling
  Work with connector suppliers to make open proposal to subgroup
Connector Definition and Enabling 2

## Slide 15: Spec Feedback/AR List
General
    Add TBD% of TDP as idle power (PCIe down, system in S5) to 3.0 spec; 50% is candidate.
    Add power sequence requirement into 3.0 spec (Roy@Mellanox)
    Request to remove P5V_AUX (John S@Dell)
    Request to remove Main rails and keep Aux only (Paul K@ Intel)
For #14
    Need to watch for opening size @ chassis face plate (Rob C@Dell)
    Mechanism of fool proof might be required to avoid removing NIC module by un-trained user
Starts to maintain a list of specific feedbacks about specification and implementation

## Slide 16: Thermal simulations
Refer to http://www.opencompute.org/wiki/Server/Mezz#Updated_doc for latest thermal discussion

## Slide 17: Mechanical discussion
Refer to http://www.opencompute.org/wiki/Server/Mezz#Updated_doc for latest mechanical discussion

## Slide 18: Design boundary survey template:

## Slide 19: Design boundary survey update 4/17:
Typical use case(90/10) Summary:
20W-30W with 105C T_case
25x25mm2 to 33x33mm2
I/O
  Dual QSFP and SFP
  Quad SFP
  Quad Base-T
80% has DRAM requirement
  6x-10x DRAM components
  ~0.4W each
Optical Module
  1.5W SFP and 3.5W QSFP
  85C T_case (industrial grade)
Environment
  Cold aisle operation with 35C ambient
  Hot aisle operation with pre-heating up-to 55C

## Slide 20: Design boundary survey update 4/17:
Stretch goal use case(50/50) Summary:
TDP wise target 30W-50W
Package size up to 45x45
Up to 20x DRAM components
70C commercial grade optical module
Hot aisle operation with pre-heating 65C-70C ambient

## Slide 21: Background
OCP Mezz v0.5 defined ~4-5 years ago:
10G Ethernet
2x SFP
X8 PCIe Gen3
I2C sideband
OCP Mezz v2.0 defined ~1-2 years ago:
10/25/40/50/100G Ethernet
Up to 4x SFP28, 2x QSFP28, 4x RJ45
X16 PCIe Gen3
NCSI Sideband

## Slide 22
In general, the community is seeing healthy adoption on both the NIC side and system side
Host side connection has path to Gen4 16Gbps
http://www.fci.com/en/products/board-to-board-wire-to-board/board-to-board/08mm-board-to-board-signal/bergstak-plus-08mm-pcie-4-mezzanine.html
Receiving many inquiries for implementation detail
Receiving feedback for “pain points”
Examples of adopters of OCP Mezz NIC form factor:
Broadcom
https://www.broadcom.com/products/ethernet-connectivity/network-adapters/ocm14102-nx-ocp
Chelsio
http://www.chelsio.com/nic/unified-wire-adapters/t580-ocp-so/
Intel
http://www.intel.com/content/www/us/en/ethernet-products/converged-network-adapters/server-adapter-x520-da1-da2-for-ocp-brief.html
Mellanox
http://www.mellanox.com/ocp/index.php
Qlogic
http://www.qlogic.com/Resources/Documents/DataSheets/Adapters/Datasheet_QOE2562_Adapters.pdf
Quanta
https://www.qct.io/product/index/Server/Server-Accessory/OCP-Network-Mezzanine-For-Server
Silicom
http://www.silicom-usa.com/cats/server-adapters/ocp-mezzanine-adapters/
Wiwynn
http://www.wiwynn.com/english/product/type/details/59?ptype=37
Zaius (Rackspace/Google)
http://files.opencompute.org/oc/public.php?service=files&t=d99c1c5aac68df38e09856f5c6e96a13&download
Status of Mezz 2.0

## Slide 23
Gates emerging use cases
Blocks further expansion of adoption
Understand the problem and solve by making changes to Mezz 2.0 specification
Board space is not enough for:
  Larger package IC
  Multi-IC solution (NIC + FPGA/processor)
  NIC with external DRAM
  Higher I/O bandwidth (more connector BW/count)
  Potential x32 PCIe
  Lack of length/width tiers like PCIe LP/FH-HL/FH
Mechanical profile is not enough for:
  10~20+W (100G NIC or other type of IC) vs. 3-5W(10G NIC)
  High ambient use cases(rear I/O, high ambient data center)
  Some optical module use cases
“Pain Points” and Problem Statement

## Slide 24
Connector placement is not routing friendly
  Connector location at opposite sides of card makes routing challenging
  PCIe routing and DRAM routing is crossing
Specification has usability challenge
  Concern about connector compatibility risks; hard to navigate through connector A,B,C and type 1,2,3,4
  Specification is incremental, and need some background of previous specifications to understand
Lack of common EMI plate to allow chassis I/O to take different Mezz NIC as FRU
Lack of definition of thermal trip protection
More “Pain Points”
IC on back of PCB

## Slide 25
We ask ourselves this question during survey to calibrate whether we are seeking problems for a solution.
Limitations of PCIe CEM form factor exist:
  Not able to use NC-SI sideband – valuable for shared NIC in all power states
  Not compatible with Multi-host NIC requirements - such as 4x clocks
  Power domain difference and standby power is limited – NIC tends to be active/partially active during S5
  Compact size of Mezz is preferred - often provide 1x extra slot for system configuration
  KR use case is not available
An OCP Mezz NIC spec with the above limitation addressed has value for NIC/system/CSP
Why not just use PCIe?
Updated

## Slide 26
Backups after this page

## Slide 27
Propose to put aside
Increase Z-height from 8/12mm to 16mm
Pros:
Most effective to help with the thermal challenge
Lowest impact to board design and compatibility
Can co-exist with other options
Cons:
Only increases Z-height and is not able to help with other use cases
Higher profile occupies more space and limits the system level configuration flexibility
16mm has higher risk on PCIe Gen4 SI
Propose to put aside due to not addressing placement which is a major pain point
Option 1
IC on back of PCB
Enumeration #1

## Slide 28
Keep connector location and Extend width
Option 2
Enumeration #2
IC on back of PCB
Propose to put aside
Pros:
Maximizes the I/O area
Cons:
Connector B is in the middle and is not able to utilize the extended space well for new NIC use cases
Takes space from the motherboard’s onboard device’s I/O
Take off this option due to lack of benefit

## Slide 29
Feedback:
#1 from a NIC vendor:
  NIC + FPGA (up to 40x40) + 5x DRAM + 2x QSFP application is able to fit in 14 layer stack
#2 from a NIC vendor:
  SoC (45x45) with 10x DRAM has a PCIe breakout challenge
  Routing of DRAM is blocked by PCIe
#3 from a NIC vendor
  PCIe routing direction in the way of DRAM routing for SoC + 9x DRAM application
#4 from a CSP:
  Need size close to FH PCIe
FH-HL 4.2” x 6.8” (3.9” x 6.6” usable) = 25.74 sq in.
3b 3.07 x 6.6 (-10%) = 18.2 sq in -> 30% less real estate
Option 3a Extend length only
Pros:
Added PCB length helps with some new NIC use cases
Able to fit 4x SFP+ and 4x RJ45 (3b only)
Cons:
More depth adds challenge to new board design to support Mezz 3.0
More complicated to design new baseboard to have mounting holes for both Mezz2.0 and Mezz3.0 (3b only)
Possible long PCIe trace adds risk to PCIe Gen4 SI
Option 3b Extend length and fill up the space
IC on back of PCB
Enumeration of #3
Put aside this option due to major cons about PCIe routing
Propose to put aside

## Slide 30
Move Connector B to same side as Connector A
Option 4a
Option 4b
Enumeration #4
Cons:
Moving connector B location prevents the new system from being able to support current Mezz 2.0
Placement-wise, it makes PCIe routing very unfavorable and very challenging on DRAM routing
Put aside this option due to negative impact without good enough long term benefit
IC on back of PCB
Propose to put aside

## Slide 31
Flip the ASIC to top side
Pros:
Solves the PCIe routing direction issue
Retains connector A/B location for best baseboard backward compatibility
Cons:
Mezz 3.0 heatsink height is very limited and even shorter than what Mezz2.0
Suggest to put this option aside
Option 5
Platform A (2OU)
Platform B (2OU)
Platform C (2OU)
Platform D (2OU)
Platform E (2OU)
Platform F (1RU)
Platform G (2RU)
Platform H (1RU)
Platform I (1RU)
Platform J (2RU)
Enumeration #5
IC on Top of PCB
Propose to put aside

## Slide 32
Pros:
Helpful for thermal (heatsink zone will be enlarged)
Helpful for placement
  PCIe routing is short
  DRAM placement is feasible
  Accommodate larger package
Potential to add one connector for x32 use cases
Possible backward compatibly for x8 card by placing Connector A at the same “Y” location
Cons – continued on next slide…
Option 6a
Option 6b
Move Connector A to the side of Connector B
Make 2x width/2x length option
Place Connect A in the same Y location as Mezz2.0
IC on back of PCB
Enumeration of #6
Propose to put aside

## Slide 33
Pros:
Carries most of the mechanical benefits from option 6 thermal
Easy modification from PCIe card for NIC vendors
A good option for stable form factor compare to #3
Cons:
Not able to support current Mezz 2.0
  Force system vendors to convert without path for backward compatibility and increase the friction of adoption greatly
  Increase frication of NIC vendor’s adoption due to lack of supporting systems
SI potential to 25Gbps
Needs NIC vendor input on:
  Is this the best option for long term NIC planning?
  Willingness to support both Mezz 2.0 and OCP NIC 3.0 form factor in a period to be defined, to encourage system vendors’ adoption of OCP NIC 3.0?
Move Connector A to the side of Connector B
Make 2x width/2x length options
Place A1 and B1 for same PCIe lane sequence as PCIe CEM gold finger
7
0
8
A1
15
B1
Enumeration of #7
Option 7a
Option 7d
IC on back of PCB
Propose to put aside

## Slide 34
Cons:
Possible routing challenge to be solved for Mezz 2.- mounting hole pattern at baseboard overlapping with Connector B in Mezz 3.0
Upper and lower x8 PCIe routing are crossing
May drive layer count depending on breakout plan and total routing layers available
  NIC vendor input is needed
Adds Risk to PCIe Gen4 SI
Option 6
Move Connector A to the side of Connector B
Make 2x width/2x length option similar to PCIe CEM
Put Connector A in the same “Y” location allows possible baseboard design to accommodate both Mezz 2.0 and Mezz3.0
A1
B1
7
0
8
0
7
15
8
A1
15
B1
Connector A allows plug in of x8 Mezz 2.0
Enumeration of #6
IC on back of PCB
Propose to put aside

## Slide 35
Pros:
Share most pros from option 6 on thermal and placement wise
Allows possible baseboard co-layout of Connector B for x16 Mezz 2.0
Cons:
Possible complication of PCIe breakout for 8 lanes in x16 NIC
  NIC vendor input is needed
Adds Risk to PCIe Gen4 SI
  NIC vendor input is needed
Challenge with Mezz 2.0 mounting hole pattern hits blocks new Connector A’s breakout
Same as #7, except that Pin B1 location is changed to be same as Mezz 2.0
7
0
15
A1
8
B1
Option 8
Enumeration of #8
IC on back of PCB
Propose to put aside

## Slide 36
Pros:
Covers 2 x16 PCIe Gen4 towards 400G
New baseboard is backward compatible with existing Mezz 2.0
Larger PCB space for double width card
Cons:
Only suitable for baseboard with side front I/O
Challenge about how to utilize PCIe lanes to 2nd PCIe
Not likely to be plug into existing system
ME alignment challenge
Takes almost all I/O space for half width board(high volume)
Heatsink space is still limited due to connector is in the way
Need feedback:
From NIC vendor for space usage of PCB
From System vendor for system implementation impact
2x Mezz 2.0 connectors side by side
Single width for light weight NICs
Double width for heavy weight NICs
Option 9
Enumeration of #9
IC on back of PCB
Propose to put aside

## Slide 37
Pros:
10a has similar PCB layout(routing and placement) as native PCIe CEM
Cons:
SI is a challenge for PCIe Gen4; 25G KR is almost impossible
Connector density(1mm pitch) lower for PCIe GF
10a adds challenge to stack height; takes about same height as 5mm stacking Mezz.
10b carries similar PCIe routing challenge
Using Right Angle native PCIe connector
Enumeration of #10
Option 10a
Option 10b
Propose to put aside

## Slide 38
Pros:
Easier insertion-removal action
Possible for module hot-swap mechanically
Good potential for easy EMI design and good servicebility
Good usage of z-height assuming both baseboard and NIC module takes 3mm as bottom side component max height, assuming using co-planer setup
Better thermal performance in general
Cons:
Having difficult to have baseboard supporting 2x different depth options; needs an extender card, similar to traditional riser.
Limited width in terms of fitting connector with same pitch and pin count
Need NIC suppliers input
  How is Network + PCIe + DDR routing?
Need system suppliers input
  Impact of the cut out size in baseboard
  For the MB cannot afford large cut out, option is to use RA connector, with the tradeoff of higher stack.
Comment
  Paul-Intel: worth to explore; maybe offset the card and baseboard and makes a new enumeration
  Challenge with Half width(Paul Artman@Lenovo) as well; hard to make it 1U half width 45-50W.
Using co-planner/Straddle mount connector in the back
Enumeration of #11
Option 11
Baseboard
Updated
Intend to move to close due to #14 has major advantage over #11
Propose to put aside

## Slide 39
Similar to Option 11 in placement, using RA / offset connector to avoid large cut out; connector type TBD
Enumeration of #12
Option 12
Baseboard
Based on #11 with difference below:
Pros:
Allows smaller cut out
Cons:
Connector in the way of air flow
Potential SI challenge for RA connector with high stacking
Propose to put aside

## Slide 40
Straddle Mount/Co-planner – side load
Enumeration of #13
Option 13
Pros:
Flexible heatsink height definition
Eliminated the complex, and discrete stacking height tradeoff
Better thermal performance in general
Cons:
Large cut out of baseboard, plus extra width for engagement
Challenging to route signal to connector
Thickness needs to be defined on both sides
Updated
Propose to put aside

## Slide 41
#14 Cut out size analysis 1
Enumeration of #14
Goal: To get a more solid feedback on this option
Summary is made for below key dimensions:
Typically I/O types,
Typical Mezz 2.0 implementation
Connector/golden finger size to fit x16+ side band
Connector/golden finger size to fit x8+ side band
Option 14
Side Views
Straddle
Mount
Right
Angle
Baseboard
w/ cutout
Baseboard
w/o cutout

## Slide 42
#14 Cut out size analysis 2
Enumeration of #14
Reference:
OCP_Mezz 2.0_rev1.00_20151215b_pub_release_3D_package
http://files.opencompute.org/oc/public.php?service=files&t=36d4cd91fd8e7cdb10660b0da833fbd6&download
I/O Types | Dimension
1x QSFP cage | 19.75 mm
2x QSFP in Mezz 2.0 | 42.75 mm
2x QSFP Cutout in Mezz 2.0 | 47.165 mm
4x RJ45 connector in Mezz 2.0 | W 61.8 mm D 24.94
4x RJ45 cut out width in Mezz 2.0 | 63.79 mm
4x SFP+ connector in Mezz 2.0 | W 58.01 mm D 44.51mm
4x SFP+ cut out width in Mezz 2.0 | 59.85 mm

## Slide 43
#14 Cut out size analysis 3
Enumeration of #14
Mezz 2.0 Card Size | Dimension
Mezz 2.0 width @ Card body, without Connector B area | 68mm
Mezz 2.0 width @ Card body, with Connector B area | 78mm
Mezz 2.0 depth, card edge to edge | 110.05 mm
Straddle Mount connector 0.6mm pitch Candidate 1 | Dimension
X16 PCIe + Sideband Golden finger | 64mm
X8 PCIe + Sideband | 
Reference:
OCP_Mezz 2.0_rev1.00_20151215b_pub_release_3D_package
http://files.opencompute.org/oc/public.php?service=files&t=36d4cd91fd8e7cdb10660b0da833fbd6&download
Updated

## Slide 44
One more round of feedback collection from System/NIC/CSPs
Work on other feedback that has yet to be addressed by the form factor change
Carry on activities and make progress in OCP Mezz NIC subgroup
  Wiki: http://www.opencompute.org/wiki/Server/Mezz
  Mailing list: http://lists.opencompute.org/mailman/listinfo/opencompute-mezz-card
  Mezz Subgroup calls: http://opencompute.org/community/ocp-calendars
  Workshops: TBD
Next Steps – 2017/2/16