## Slide 2: OPEN CLOUD SERVER- PROJECT OLYMPUS- JBOD
Bruce Hoch/Senior Mechanical Engineer/Microsoft
Sage Shih/Hardware Engineer/Quanta Computer
March 09, 2017

## Slide 3: OVERVIEW
4U JBOD
  88 Hot-plug HDDs
  N+1 Dual Rotor Fans
  N+N Redundant, 1650W 3-Phase, Hot-Swap PSUs
  Drawer design – slide out for service
Robust Feature Set
  Integrates into Project Olympus Infrastructure through Universal PDU
  Runs on OpenBMC
    Gathers HDD temps and component status info
  Individual HDD on/off to minimize NTF

## Slide 4
  Controlled by Project Olympus Server
    Configurable with 1, 2 or 4 head nodes
    HDD Bay segregated into 4x 22HDD Zones
  Supports SMR, HAMR, & 12Gb/s single port SAS near-line HDDs
    1.2PB/Chassis (14TB/HDD)
    9.6PB/Rack in Cold Storage Configuration (8x JBOD/Rack)
  Designed to optimize performance and reliability
    Minimized Rotational Vibration and Acoustic Noise
      <5% HDD Performance Degradation
    Maximum HDD Case Temperature ≤ 51°C
OVERVIEW

## Slide 5
Tool-less Accessible, Hot-swappable Components
  Cam Action Tool-Less Installed HDD Carrier
  Top Loaded Cam Action PSUs
  Pinch and Pull Tool-Less Fan Module
LEDs for quick failed component identification
Cold-Aisle, In-Rack Active PCA Serviceability
  All active boards are accessible for service with unit in rack
  Serviceable BMC
  4x Independently serviceable expanders
SERVICEABILITY

## Slide 6
SERVICEABILITY
Tool-less Accessible, Hot-swappable Components
  Cam Action Tool-Less Installed HDD Carrier
  Top Loaded Cam Action PSUs
  Pinch and Pull Tool-Less Fan Module
LEDs for quick failed component identification
Cold-Aisle, In-Rack Active PCA Serviceability
  All active boards are accessible for service with unit in rack
  Serviceable BMC
  4x Independently serviceable expanders

## Slide 7
SERVICEABILITY
Tool-less Accessible, Hot-swappable Components
  Cam Action Tool-Less Installed HDD Carrier
  Top Loaded Cam Action PSUs
  Pinch and Pull Tool-Less Fan Module
LEDs for quick failed component identification
Cold-Aisle, In-Rack Active PCA Serviceability
  All active boards are accessible for service with unit in rack
  Serviceable BMC
  4x Independently serviceable expanders

## Slide 8
SERVICEABILITY
Tool-less Accessible, Hot-swappable Components
  Cam Action Tool-Less Installed HDD Carrier
  Top Loaded Cam Action PSUs
  Pinch and Pull Tool-Less Fan Module
LEDs for quick failed component identification
Cold-Aisle, In-Rack Active PCA Serviceability
  All active boards are accessible for service with unit in rack
  Serviceable BMC
  4x Independently serviceable expanders

## Slide 9
  External mini-SAS HD cables route directly into enclosure
    Reduces number of interconnects, improving SI
    Eliminates need for repeater and ultra low-loss PCB materials
  Static lid and outer chassis shell
    Reduces services steps and cost
    Facilitates blind-mate rack integration
  Side Loaded independent HDD/Expander boards
    Expander integrated onto HDD board
    Improves cooling efficiency
    Reduces number of interconnects for improved SI
A/C Power Cable Chain
SAS Cable Chain
HARDWARE ARCHITECTURE

## Slide 10
  External mini-SAS HD cables route directly into enclosure
    Reduces number of interconnects, improving SI
    Eliminates need for repeater and ultra low-loss PCB materials
  Static lid and outer chassis shell
    Reduces services steps and cost
    Facilitates blind-mate rack integration
  Side Loaded independent HDD/Expander boards
    Expander integrated onto HDD board
    Improves cooling efficiency
    Reduces number of interconnects for improved SI
HARDWARE ARCHITECTURE

## Slide 11
  External mini-SAS HD cables route directly into enclosure
    Reduces number of interconnects, improving SI
    Eliminates need for repeater and ultra low-loss PCB materials
  Static lid and outer chassis shell
    Reduces services steps and cost
    Facilitates blind-mate rack integration
  Side Loaded independent HDD/Expander boards
    Expander integrated onto HDD board
    Improves cooling efficiency
    Reduces number of interconnects for improved SI
HARDWARE ARCHITECTURE
Expanders

## Slide 12
  External mini-SAS HD cables route directly into enclosure
    Reduces number of interconnects, improving SI
    Eliminates need for repeater and ultra low-loss PCB materials
  Static lid and outer chassis shell
    Reduces services steps and cost
    Facilitates blind-mate rack integration
  Side Loaded independent HDD/Expander boards
    Expander integrated onto HDD board
    Improves cooling efficiency
    Reduces number of interconnects for improved SI
HARDWARE ARCHITECTURE
HDD Row Spacing Front View

## Slide 13: FIRMWARE ARCHITECTURE
  Block Diagram
DCM
Runs on OpenBMC

## Slide 14: THERMAL ARCHITECTURE
Supports 88x 14W HDDs & 4x 16W Expanders
Air-flow management reduces temperatures
  Multiple by-pass air channels to feed rear rows cold air
  HDD temperature ≤51C with failed rotor and 35C inlet
  Minimizes required total chassis airflow
4x N+1 dual rotor fan modules
  Performance targets supported in failed rotor case
  Supports up to 5-minute hot service
Isolated PSU cooling – No HDD to PSU pre-heat

## Slide 15: HDD PERFORMANCE
Maintains ≤5% throughput degradation due to self-excitation and external vibration
External Vibration Isolation
  Chassis architecture reduces mechanical and acoustic transmitted vibrations
  Configurable option to add acoustic damping material to limit transmission of high frequency broadband noise to rear row of HDDs from fans
Thermal algorithm will minimize fan rpm with consideration to HDD performance

## Slide 16
Maintains ≤5% throughput degradation due to self-excitation and external vibration
External Vibration Isolation
  Chassis architecture reduces mechanical and acoustic transmitted vibrations
  Configurable option to add acoustic damping material to limit transmission of high frequency broadband noise to rear row of HDDs from fans
Thermal algorithm will minimize fan rpm with consideration to HDD performance
HDD PERFORMANCE

## Slide 17
Maintains ≤5% throughput degradation due to self-excitation and external vibration
External Vibration Isolation
  Chassis architecture reduces mechanical and acoustic transmitted vibrations
  Configurable option to add acoustic damping material to limit transmission of high frequency broadband noise to rear row of HDDs from fans
Thermal algorithm will minimize fan rpm with consideration to HDD performance
HDD PERFORMANCE

## Slide 18
Maintaining low HDD case temperatures
Developing architecture that allows for in-field servicing
Providing <5% HDD performance degradation in all operating conditions
Achieving 12G/s SAS signal speeds without using a repeater
ACHEIVEMENTS